## Slide 1
Network Technologies for 2030 Networks
Delivering the Promise
of Future Media by 2030
Toerless.Eckert@Futurewei.com, Santa Clara, CA, USA
IEEE International Conference on Cloud Networking
6. November 2019, Coimbra, Portugal

## Slide 2: Technologies for 2030 Networks
WHY
more users, (IOT) devices, quality, critical/future applications, …
WHERE
Metropolitan network infrastructures (fixed/mobile) (for this slide deck)
WHAT
New network protocol/services technologies
NewIP, High-Precision, Qualitative Comms, Holographic, …
....
GREAT SUCCESS ! ??

## Slide 3: WHERE: from Internet to ManyNets
User
Service
SP1
SP2
The Internet
One network to rule them all
SP3
SP4
Internet: Global Connectivity, Best Effort
transit
TCP/IP was/still-is designed for multi-transit Internet (1970th)
Since ca. 2010:
  Scaling global services requires Edge Data-Center (Cloud)
  Raise of global ASP, peerings, cloud services, Death of transit
Users
Access SP
Users
Metro Nets
Peering, Interconnects, Hosting
SP and ASP global backbones
DC
DC
DC
DC
DC
DC
DC
Private Networks
Users
Manynets: private (global) backbones
Devices
Devices

## Slide 4: WHERE: 2030 Internet Front-haul / Backhaul
Users
SP access networks
Users
Metro Networks
Private Networks
Users
Edge-Cloud(s)
public, private, telco
“private” ASP (content + app sync distr.)
“private” Content Provider (caching, streaming)
“public” ISP global backbones
Internet transit backbone
OTT Content/App. provider “backbone”
Access
High Precision Fron-thaul
ManyNets/Transit Backhaul
Space Networks – public / private
space networks extending to users
Global Backbones
Private (physical, OTT/Internet), “public”
Traditional Internet / transit traffic: best effort, > 20 msec RTT
2030: High Precision traffic
2020: 70% visible user traffic
Exchanges
Edge
DCs
Edge
DCs
Interconnects
Peerings
Devices
Devices
ASP and Internet Transit traffic

## Slide 5: Network 2030 Internet Front-haul Opportunity for better services
Transit has no business relationship with neither user nor service
  Key reason for current Internet to be limited to “Best Effort” (BE) services
Fronthaul can be architected without transit.
  Key enabler for better than BE services in 2030 networks.
  User/Service <-> User/Service: 2 networks + interconnect.
Geographical limits (e.g.: 100 mile diameter) of Front-haul permits latency critical services.
  Limited physical latency (low msec).
User
Service
SP1
SP2
SP3
SP4
Internet: Global Connectivity, Best Effort
transit
Users
SP access networks
Users
Metro Networks
Private Networks
Users
Edge-Cloud(s)
public, private, telco
Access
Exchanges
Service
Interconnects
Peerings
Devices
Devices
Service
The Internet
One network to rule them all
Internet 2030 Fronthaul

## Slide 6: Technologies for 2030 Networks Refined 2030 Network Solutions Dependencies
WHY
WHERE
WHO
Develops 2030 Network services
Operates 2030 Network services
HOW
What technologies do we need to enable WHO ?
WHAT
…
GREAT SUCCESS !!???
Forgot
Something

## Slide 7: WHO: Enable Innovation & Opportunity
Cloud drives Innovation & Opportunity
  Software-ization is enabler for new Service Developers and Services Operator
  DC-networks: becoming softwareized (P4,..)
Telco-Cloud => Software
  5G ‘Network’, VPN, Security, Content services
  MVNO, SD-WAN, ..
  But Software is not 100Gbps…Tbps
Metro-Wireline Networks ?
  Today: Speeds, Feed, Commoditization.
Key Technology gap:
  Software-izable Tbps Internet 2030 access networks
SP access
Metro
Private
Internet 2030 Fronthaul
Service
Service
Service
Service
Innovation rich
Innovation poor
Data-centers
Exchanges
Interconnects
Peerings
Mobile
Users
Users
Users
Devices
Devices

## Slide 8: HOW: Software-ized Metro-Network
How to deploy & sell new network forwarding plane ?
Slices do NOT allow to program new forwarding planes
Overlays - VMs / Containers in Data-Center
No “bare-metal” option (hop-by-hop) on a metro-network (*)
Example (from last decade): Inability of ICN to get deployed
Overlay enough for many network services, but not all:
Speed/Performance, Data-replication,
Latency sensitive: High-Precision, Deterministic, Coordinated, Qualitative, Lossless
Software-ization of Tbps forwarding plane: challenges for a decade
Flexible programming languages (P4 too limited)
Chip cost / power consumption
Virtualization: context overhead VM->Container->Lambda model
Programmable QoS (packet scheduling)
Resource Management (absolute vs. relative)
Innovation Bottleneck
Innovation Above, Below, and Alongside
But, Limited Innovation “Inside” the ’Net
Inside of the network needds to change
We Are Desperate to Innovate Inside
Jennifer Rexford,
ACM Sigcomm 2018 Keynote Speech
(*) Commercial offerings, not talking about research networks from NSF.

## Slide 9: Technologies for 2030 Networks
WHY
WHERE
WHO
HOW
WHAT
Current Internet/private network experience “challenged”
Big Packet Protocol
Coordinated Communications
High-Precision Communications
Qualitative Communications
Lossless Networking
Preferred Path Routing
GREAT SUCCESS !!!!?

## Slide 10: BPP – Big Packet Protocol Architecting the next-generation forwarding plane
Network evolution so far:
Primarily evolution of management/(control) plane
Very complex , incrementally grown forwarding planes:
Duplicating efforts, limited in flexibility, Little/not App-“programmable”
Various bad limitations. E.g.:
IPv4 / IPv6, per-feature extension header, parameters per-hop SRv6
fixed size addresses, minimal changeable by network, …
MPLS, fixed size addresses, hacked bottom of stack parameters,…
Ethernet, often same or better QoS features than IP/IP, but all different.
Programmable networks / slices / 2030 services (high precision,..)
Very challenging (if not impossible) to build well within this maze
Can we design / frame a better, unified forwarding plane ?
Unify / superceed existing solutions, extensible
(SLO) “Service Level Objective” based – “Do What i Mean Networking”
Without all the boring bits of history
Traditional
networks
SDN
NFV & SFC
BPP
Physical servers
Containers
Serverless
(“Lambda”)
VM – IaaS, PaaS
“Networkless ?!”
Application/DC vs. Network evolution
Better

## Slide 11: BPP – Big Packet Protocol Key architectural aspect for flexibility
Actions, Parameters and Metadata
Actions (Commands) as Unit of forwarding plane extensibility
Per action parameters, but cross-action shared metadata (to minimize headers)
Explicit indication of sequentialization / parallelization of actions
Flowlets: Integrated state-full and state-less Actions
Per flow actions minimize per-packet header
Per-packet actions allow scale to arbitrary number of flows in network.
Not all actions can be performed per packet, e.g.: limit rate to X Mbps
Efficient stacking or merging of headers
Generalization of MPLS/SR concept for efficient layering / tunneling
Look-ahead across multiple headers ?
Support for different address lengths
128 bit too long/inefficient for most private networks , IoT, replace existing solutions
Many open design issues – translation / integration, multiple instances, assignment authorities, …
Config Interface
Output Interface
Routing
Protocols
Transport
Resilience (ISSU) …
FIB Tables
Policies
Receive
Process
Transmit
ASIC
Management
Control
Data Plane on LC
Monitoring
Agent
Management Interface Agent
BPP Processing
Forwarding Ctrl Interface
BPP Engine
Stateful BPP Info Storage
Queues
…
BPP Rules/Policies
Command header
Action “increment”
Action (contd.)
Metadata
Command header
Condition
Cond (contd.)
Action “drop”
BPP Header
Ver 1
X
F
e
0
v
0
ea ignore
len 21
meta
20
r
parameter
metadata total-q-d (offset 0)
len
7
n
1
s
1
c
0
p
0
action
increment-by
n
00
len
6
r
np
2
sp1
1
sl1
01 (meta)
next proto
total-q-d 0
parameter
data item: e-q-depth
spn
0
sln
0
sp2
1
sl2
11 (data)
len
9
n
0
s
0
c
1
p
0
ctype
> (“gt”)
n
0
c
00
len
5
np
2
sp1
1
sl1
01 (meta)
spn
1
sln
00 (value)
parameter
value: 200
parameter
metadata total-q-d (offset 0)
p
0
action
drop
n
00
len
3
r
np
0
sp1
0
sl1
01

## Slide 12: The Internet: Best Effort (throughput)
What is Internet (throughput) fairness ? “all flows are created equal” ??? E.g.: competing 4K TV and Smartphone Paying more will not get you more throughput during congestion
How to achieve fairness ? Path-RTT, transport-protocol-aggressiveness
Guarantees ? Absolute reservation == scale issues Relative throughput easier !!
Limited by Loss and Capacity: Higher performance requires lower loss or higher overhead
Lousy
Internet: Best Effort
“Best Effort” Per-Hop Behavior (PHB)
ECN / AQM (maybe)
“Shortest Path” routing
Throughput / Priority Guarantees
Latency Guarantee (path/queuing)
No-Loss guarantees
Jitter

## Slide 13: Rich QoS services in private IP networks
DiffServ in L2/L3 VPN / enterprise / DC
How do you calculate class-weights ?
Time dependent ?
Four-level Hierarchical (DiffServ) QoS.
One off SP / content provider hacks.
ACL for SP video
Co-location of OTT content servers in SP network
Different IP / MPLS / Ethernet QoS
Mapping nightmares, service/functionality loss
Per-flow “IntServ” services
  Great for limited private networks, but does not scale to metro networks hop-by-hop
Archaic
configuration
nightmares
Beyond Internet:
D& ifferentiated Services
Integrated Services

## Slide 14: Analyze applications Understand how network service: (throughput, loss, latency) impact user experience
Not even good MOS for AR/VR today! MOS = Mean Opinion Score
Initial , intermittent buffering
Probability / periodicity of non-congestion loss (NCL) Random (bit /packet errors) vs. Burst (outage) loss
Ability to conceal NCL (codec dependent) Ability to correct NCL (FEC, retransmissions)
Normal/Ideal quality (throughput)
Quality Variation by throughput variation Frequency, fine-grained (concealed)
Congestion Loss (*YUCK*), Self-Friendly-ness
Use-case: Digital Actor Single point cloud holographic object in a real scene

## Slide 15: Coordinated Communications
Synchronized latency experience “Why can player 3 shoot /kill faster?”
(lowest RTT to server)
In-network latency fairness (vs. clients faking RTT)
Aggregate Network Resource Management
“Get N Gbps for 2 hours, split across parties as you like”
Scale optimizations with guarantees
Multicast: in-network replication to parties
Incast: Many to “virtual/cluster” one
Coordination may need to happen on many hope, or (depending on coordination function) on the edge of the network.
Use case: Synchronized Multi-Part Remote Collaboration

## Slide 16: High-Precision Communications SLO (service level objective) based latency management
Let applications manage network latency (queuing, buffering)
End-to-end min..max latency control
Stateless == per-packet
Avoid scale limits of network flow-awareness
With/without (bandwidth) reservations E.g: dynamic adjust throughput, but keep low-latency
On-time: Delay early packets Reduces application side buffering / jitter
In-time Guarantees
On-time Guarantees
Use case: Latency sensitive streaming, control-loops

## Slide 17: High-Precision Communications Example: Flows with different path length/hops
Typical metro network ”core” ring part with aggregation
Fair-latency for Flow 1 / Flow 2 ?
  Flow 1 disadvantaged by physics (path latency, hops)
  But can compensate with high precision communications:
Edge-coordination function: Assign same minimum end-to-end latency to both flows
  Somewhat larger than flow 1 physical propagation latency.
  When there is no contention: This just “delays” flow 2 packets in network to create fairness
Interesting under network contention/congestion
  Intelligent latency aware queuing (node B, C) would know from BPP header that flow 2 packets have more time to spare in queuing… And dequeue flow 1 packets faster
Path/end-to-end latency based automatic queuing priorities.
Use case: Latency sensitive streaming, control-loops
Destination 2
…
Sender1
Destination 1
Sender2
…
100x
100x
A
B
C
D
E
…
100x
…
100x
…
100x
queue
queue
queue
queue
Flow 1
Flow 2

## Slide 18: Qualitative Communications
Layered/Object media codecs / transport
e.g.: MPEG SVC, ALC RFC5775
Network awareness of Quality
Mapping to different per-packet network resources
E.g.: congest/(discard) highest-quality level first
Redundancy:
L3 In-network redundancy (FEC) insert/remove
From flows to packets:
When bitrates increase but not packet rates E.g.: Optical Switched Networks => huge packets
Packet-Chunks, tail-discard / congest / recover
Qualitative Packet
Noisy link
Congested Node
Congested Node
Congested Node
IP HDR
Use case: Scalable Gradual management of quality

## Slide 19: 2020 State of Traffic Engineering
MPLS/RSVP-TE designed for Traffic Engineering (TE)
  Traffic flow resource guarantees: bandwidth, latency, reliability
  AC with path selection, FRR protection (sub 50ms), per-path/(hop) QoS
  Complex, scaling limited for last two decades dominant use-case:
Capacity optimization
  Maximize use of non-ECMP SP paths for best effort traffic
Segment Routing (SR-MPLS, SRv6)
  Revives 1981 “loose source-routing”. Ideal for capacity optimization.
  Simplifies routing architecture: Only IGP (ISIS, OSPF), no LDP.
  Rightfully replaces RSVP-TE for capacity optimization
Source-routing not ideal for real TE problems
  Header tax, undesired re-routing, per-hop-guarantees, monitoring
  Difficult/impossible to apply to arbitrary forwarding planes
2030 Networks need to support real TE solutions
  With similar optimization as SR did for capacity optimization
Per-hop header tax (MPLS) SR vs.
Per-flow state based solutions (e.g.: RSVP-TE)
Non-equal-cost-path traffic steering
RSVP-TE SR-MPLS

## Slide 20: Lossless networking and path steering
Live-live: “near zero loss”, no added latency
  Send two copies of same traffic across “disjoint” (no shared failure) paths
  Used since 1990th for financial, military, video (SMPTE since 2010th)
  All redundant networks have >= 2 disjoint paths. Value of critical traffic easily >= 2 * normal best effort traffic.
PREOF – Packet Replication Elimination Ordering Function
  DetNet term for live-live solution. TSN also uses this.
  Only working there in simpler topologies than those needed for 2030
(SR) Loose path-steering issues
  Unexpected / unnecessary rerouting: When one path fails, rerouting it undesirable – but unavoidable with loose paths.
  Header tax redundant when per-hop state needed anyhow:
  Strict latency management (DetNet, TSN) (“shaping state”)
  Monitoring / Diagnostic state, MTU
Real networks have long, complex paths
  Especially in metro-space (up to 30 hops)
  Special solutions for rings insufficient
A1
A2
A3
A4
A5
A6
A7
A8
Source
Traffic copy 1
Traffic copy 2
SR label
hop
Live-live transmission
In ring with SR
A1
A2
A3
A4
A5
A6
A7
A8
Source
Traffic copy 1
Traffic copy 2
SR label
hop
Rerouting under Failure
SENDER 1
SENDER 2
RECEIVER 1
RECEIVER 2
Sender sends same data twice, red and green
link/node failure interrupt only one copy of data

## Slide 21: PPR – Preferred Path Routing
Core/P-nodes
Edge/PE-nodes
centralized Path Computation Engine (PCE)
distribution / flooding
decentralized
PCE
decentralized
PCE
decentralized
PCE
IGP
Area/Domain
L2/IP Router FWD Plane
Fully backward compatible + extensible, lean path routing information on the Wire
L2
Future
IP/L2 Packet
IP/L2 Packet
Simple FIB
Shortest Path/Best Effort
Novel Control-plane Signaling Architecture
    Use IGP to signal TE information / replace RSVP-TE
    PCE / AC (Path Computation Engine / Admission Controller) to network
    Centralized PCE/AC or decentralized (edge nodes)
  Unified for current and future forwarding planes
    Strict/loose forwarding entries: IPv4, IPv6, SR-MPLS, Ethernet, future
    PPR-ID: Identifier for a path == forwarding plane address
    /32 for IPv4, /128 for IPv6, /20 for SR-MPLS,…
    Per-hop QoS setup as necessary/desired
    SW-update-only for existing forwarding planes
  Orthogonal / combinable with SR
    PPR when hop-by-hop state required.
    SR for lightweight capacity maximization.
  All the benefits of RSVP-PE without the limits
    Efficient signaling via IGP instead of heavy hop-by-hop on-path
    RSVP-TE only for MPLS forwarding plane.

## Slide 22: PPR Graphs – scaling state
Point 2 point paths N2 scaling issue
    Worst case: network wide path optimization N source to N dest.
    Full mesh NxN paths (RSVP-TE) . N2/k path across single node
    SR: N*l source-route stacks in headers on each source node + N’ SID state
    k = number of parallel path in network, l = average number of hops in network
  PPR can signal “Graphs” from PCE to network
    Aggregate per-hop-state whenever possible (determined by PCE)
    No change in forwarding plane. Still simple “destination” forwarding entries
  PPR-Tree
    (Sub)set of senders in network to one destination.
    Multiple Trees to same destination for different policies easily possible.
    Set of 1 tree for each destination like a “Flex-Topology”, but with paths calculated by controller – easier than reverse-engineering SPF metrics.
  PPR “Forest”
    Shared graph for multiple destinations.
    Allows for minimum amount of state in network, e.g.: for live-live services
    Controller calculated path == better live-live paths than distributed MRT live-live
PE3
PE4
PE5
P1
L1
P2
PE1
PE2
P7
P4
PPR Tree: all possible sender to destination PE5
PE3
PE4
PE5
P1
L2
P2
PE1
PE2
P7
P4
Better PPR Tree for some subset of sender
2 PPR Forests representing any path in ring topology
Sender
Dest
PPR Forest 2
clockwise
PPR Forest1
A1
A2
A3
A4
A5
A6
A7
A8
counter
clockwise
A1
A2
A3
A4
A5
A6
A7
A8
Sender
Dest

## Slide 23: Technologies for 2030 Networks
WHY, WHERE, WHO, HOW, WHAT
GREAT SUCCESS !!!!!
But wait… there is more (to do)

## Slide 24: Vision Network 2030
Network 2030
New Media
New
Services
New
Infrastructures
2D
3D
2 Senses
5 Senses
Gbps
Tbps
MS
Sub-MS Latency
Lossless Networking
High-Precision Communications
Holographic Type Communications
Converged Terrestrial and Space
Fidelity and Trust
Federated Networks
Next wave of
Internet Innovations
Holographic Society and Industry
OneNet ManyNets
Mbps Gbps/Tbps Access
Computing in Networks

## Slide 25: Publications and Talks
Concepts
  A New Way to Evolve the Internet, A Keynote Speech at IEEE NetSoft 2018, Montreal, Canada, June 2018
  What if we reimagine the Internet?, A Keynote Speech at IEEE ICII 2018, Bellevue, Washington, USA, Oct 2018
Framework and Architecture
  A New Framework and Protocol for Future Networking, ACM Sigcomm 2018 NEAT Workshop, Budapest, August 20, 2018
  New IP: Design for Future Internet with New Service Capabilities Envisioned, IEEE ICC Industry Tutorial, 2019
Market Drivers and Requirements
  Towards a New Internet for the Year 2030 and Beyond, ITU IMT-2020/5G Workshop, Geneva, Switzerland, July 2018
  Network 2030: Market Drivers and Prospects, ITU-T 1st Workshop on Network 2030, New York City, New York, October 2018
  Next Generation Networks: Requirements and Research Directions, ETSI New Internet Forum, the Hague, the Netherlands, October 2018
  The Requirements for the Internet and the Internet Protocol in 2030, ITU-T 3rd Workshop on Network 2030, London, Feb 2019
New Technologies
  Preferred Path Routing – A Next-Generation Routing Framework beyond Segment Routing, IEEE Globecom 2018, December 2018
  Flow-Level QoS Assurance via In-Band Signaling, 27th IEEE WOCC 2018 , 2018
  Using Big Packet Protocol Framework to Support Low Latency based Large Scale Networks, ICNS 2019, Athens, 2019
Use Cases and Verticals
  A Novel Multi-Factored Replacement Algorithm for In-Network Content Caching, EUCNC 2019, Valencia, Spain
  Distributed Mechanism for Computation Offloading Task Routing in Mobile Edge Cloud Network, ICNC 2019, Honolulu, USA
  Enhance Information Derivation by In-Network Semantic Mashup for IoT Applications, EUCNC 2018, Ljubljana, Slovenia
  Latency Guarantee for Multimedia Streaming Service to Moving Subscriber with 5G Slicing, ISNCC 2018, Rome, Italy

## Slide 26: References
Holographic content considerations methods for efficient data transmission and content creation methodologies
Point Cloud Compression in MPEG MP20 Workshop Hong kong 2017
Keynote: the near future of immersive experiences: where we are on the journey, what lies ahead, and what it takes to get there.
Architectures and codecs for real-time light field streaming journal of imaging science and Technology , January 2017
A Dynamic Compression Technique for Streaming Kinect-Based Point Cloud Data (2017 International Conference on Computing, Networking and Communications (ICNC): Multimedia Computing and Communications)
Technical White Paper on Mobile Bearer Network Requirements for Mobile Video Services.
On the Support of Light Field and Holographic Video Display Technology, Light Field Lab, Inc., San Jose, CA. “The road to immersive communication,” Proceedings of the IEEE, vol. 100, Apr. 2012.

## Slide 27
Comments, Curious, Questions?
Toerless.Eckert@futurewei.com
Thank You