## Slide 1: Unified Forwarding Plane for Enhanced Services
NIPAA - Session C
https://icnp20.cs.ucr.edu/nipaaprogram.html
Time: Oct. 13, 2020, 3:30 p.m. to Oct. 13, 2020, 5 p.m. (CEST)
Toerless Eckert, Toerless.Eckert@futurewei.com, Futurewei
Stewart Bryant, sb@stewartbryant.com, Futurewei & Univ. Surrey

## Slide 2: Abstract
Research into the evolution of IP forwarding is proposing enhanced end-to-end, per-hop services in support of requirements by current and even more so future applications, such as high-precision latency, qualitative and deterministic forwarding.
When such an evolved IP forwarding plane would be were deployed In a similar manner to as todays IP/IPv6 forwarding plane, these enhanced services would not be able to operate on every hop though, because todays network paths are built as a mix of L2 ethernet witching, L2.5 MPLS switching, L3 routing and various forms of "tunneling" especially in mobile networks.
A more fundamental study is therefore needed to understand how the new requirements are best met, and how we can migrate the network from the network of today to a network that can meet the new needs.
This talk is about ongoing work, it is meant to inspire attendees to think bout this area no results will be presented

## Slide 3: New Services require New Forwarding
25 years ago: IPv4 -> IPv6
  and all we got are more addresses ?!
  Other foundational goals of IP-NG effort leading to IPv6 not adopted with IPv6
  Fundamentally: 50 year old protocol / services model
What Future IP Evolution (FIPE) do we need ?
  IPv6 Forever ? New IP ?
  Will never know ... until we explore the options and compare:
    Best option with IPv6 (IPv6 “Law”: RFC8200) + Extensions
      See IETF work on source routing extension headers: Small changes, decade of work...
    Best option for packet headers/design without these constraints (NewIP)
  Compare
    Likely: When urgent need and feasible: improvements will be “hacked” into IPv6, but “cleaner” / “better”? solution possible when not constrained by RFC8200 limits

## Slide 4: “Network Layer” (Hop-by-Hop) Services actually: applies to (L2, L2.5, L3, L3.5), not only “network layer”
Services are Functions of the forwarding plane that…
  May happen on every hop supporting the service (hop-by-hop)
  Are indicated / desired by the endpoints (user) (?!!!!)
  Impact / Differentiate the traffic experience
    absolutely or relative to other traffic
Distinction “Service” vs. “Function” example: Traffic Steering / Source Routing:
  Widely used in SP networks for “Capacity Optimization”: Networks steer traffic flows load-based around different, non-equal cost paths. Maximizes Return of Investment (RoI) of network infrastructure
  If applied to all traffic equally traffic steering is just a “function” as it does not meet 2, 3.
  If different user traffic would indicate different goals resulting in different steering results, then the steering becomes part of a service:
  Example: “low-latency” == steer across ”shortest path with metric=latency”: less bandwidth but lower latency

## Slide 5: IP Services
8 bit TOS/TC = (DSCP, ECN) field in IPv4/IPv6 header. 30++ year old architecture
ECN (2 bits in TOS field): Fast congestion signaling
  Limited, challenging service model
DiffServ (6 bits of TOS field):
  Per-packet services
  Locally significant indication of “traffic class”. Limited standardization of semantics, no use outside of “controlled” networks. Many abuses
IntServ (Integrated Services)
  Per-flow service (flow = IP 5-tuple)
  Service established through signaling. SDN or on-path (RSVP, {NSIS})
  Only option today to support Guaranteed Services for traffic flows
    Guaranteed Bandwidth, Guaranteed maximum end-to-end latency
    Very little adoption / deployment
    IETF DetNet effort raises need to support this again
No fundamental recent Stds. improvements of this ca. 25 year old framework
  Many signaling refinements to RSVP in the last 20 years, some new DSCP classes too
  But nothing beyond “classes”

## Slide 6: New (IP Services) – our vision, How: Contract header / BPP
New header in packets to specify flexible extensible services
  Tentatively called “Contract” header
  Ongoing prototype work for New IP header architecture
Rethink encoding/programming of services packet header:
  Service expressed through action commands with parameters in header
  Additional metadata: shared data elements not tied to individual actions
  Explicit indication of sequentialization / parallelization of actions
  Multiple encoding options for same functional outcomes
  “Statelets” for “per-flow” actions
    BPP header as “in-band/in-packet” signaling replacing RSVP
  Scalability beyond flows with per-packet services/actions
    E.g.: SP core networks would require millions of flows

## Slide 7: New (IP Services) – our vision, What: High Precision Communication services
Beyond 8 bit “QoS“ in packets
  what could/should services be: existing / new research how would/could it be expressed in network header:
Congestion Control (CC)
  ECN vs. PCN - currently use same bits to signal, but deliver different experience.
  More than 2 ECN bits for faster CC level signaling (LIVE research paper)
  Upspeeding indication (minimum free path bandwidth ?!)
Throughput
  Explicit signaling associated with difference in target bandwdidth e.g.: as possible in NADA (weight)
  signaling of flow-bandwidth for stateless weighted fair queuing (DPS research 2010)
Loss
  Signaling of discard priority (known benefits for video, e.g.: I/P/B differentiation – payload encrypted.
  Signaling of flow copy MRT/Live-Live high-resilience deployments. sub-flow ?
  Sequence number (as required by PEROF DetNet, not existing for IP)
Latency
  latency SLO , end-to end min/max, experienced latency, (see NOMS LBF paper)
  signaling of experienced latency for better per-hopp-functions
  discard packets early when they are too late (not based on hops)

## Slide 8: Side note New (IP Services) – our vision, more
For reference (Not relevant for rest of presentation)
Qualitative Communications:
  Beyond per-packet contract headers to indicate different services for different chunks in packets
New path steering architecture (PPR)
TBD: Unified destination representation (beyond unicast)
  Send packets to individual-destination, named-group-of-destinations, member-of-a-group, enumerated-group-of-destinations, …
    Aka: unification of current “historically evolved” approach in IP to deal with unicast, anycast, multicast, BIER – and beyond

## Slide 9: Most Networks are multi-layer
…
And QoS/service-actions across different layers vary widely today
  See e.g.: mapping DetNet (IntServ)  TSN
IP DSCP =~ Ethernet COS =~ MPLS EXP
Sufficiently different to make any deployment painful when more than Best Effort desired
Mapping == lowest-common-denominator
Main “working” deployment model
  Lower layer QoS is just “aggregate”, “coarser” service than higher layer
  But this model can not provide high-precision across lower-layer hops
L2Switch
L2Switch
Host
Host
Host
Host
…
Router
Router
…Backbone..
Router
Router
Host
Host
Host
Host
LAN
pre-1990’th or abstracted view
Simple current reality
IoT / industrial / Enterprise
…Backbone..
service
action

## Slide 10: Multiple forwarding layers: Ignore / eliminate / embrace ?
IP/IP6 towards hosts require “Ethernet LANs”
  Separate IPv6 subnet per host unmanageable
  IP/IPv6 subnet with more than 1 host or more than 2 routers have “L2 switching” requirements
    Even when they are hidden inside a single box called router
Ignore: (Personal) grievance from 1980th… 1990th :
  ISO CLNP was designed to eliminate need for L2 switching
  1990th IP-NG could have adopted this. But IPv6 did not!
  CLNP address (NSAP) “host routes” instead of L2-MACaddr “routes”
    ES-IS NSAP addr assignment, IS-IS L1 “host-routes”
Eliminate: Can be done with IP(v6) as well… but challenging
  IPv6 link local address space =~ LAN, but adds no benefits of MACaddr, but adds IPv6 complexities
  Ethernet is attractive because of auto-addressing, auto-config / switching. Not defined for IPv6!
  Some IPv6 network architectures use host-routes: IoT/RPL, Autonomic/ACP/RPL
Embrace: Forwarding protocol with multiple address sizes could be reused across layers
  ‘L3’ instance using e.g.: 128 bit addresses – or 32 bit addresses (why longer than needed) !
  ’L2’ instance using e.g.: 48 bit addresses (or 16, 20, 24, 64...)
If/where we embrace multiple forwarding layers:
  How to deal with services and their packet headers ?
routing
Every access router is a mixed
L2/ethernet + L3 IP router device
Router
IP subnet
IP subnet
Host
Host
Host
Host
IP subnets ~= VLANs =~ L2 switching
Please do not ignore
the elephant!

## Slide 11: Multiple layers … and Contracts / Services
Protocols evolved from solving different problems providing different services.
  Ethernet… MPLS... SRv6 .. IP/IPv6
Historically, protocols where designed to do as little as necessary
  Solution for the problem where pre-existing protocols have a gap
  ‘Simply’ layer multiple protocols to solve multiple problems
  No Black & white: often good, often problematic
Main challenge: re-inventing High Precision Services for every layer
  Repeatedly solving the same problems... Incompatible to each other
  Such as per-hop actions for (QoS / high precision communication) services
  Duplicating efforts
  Slowing down adoption of those services
Explore what a future forwarding plane protocol needs to support so it can be re-used across multiple layers easily
  Needs to have a superset of services required at different layers
  Should be backward compatible/interoperable for migration/investment protection

## Slide 12: “Contract” header options
Todays “correct” / “dogma”
  Every layer has it’s own contract header
  Mapping, duplication of standardization, loss of functionality,…
Todays “Layer violations” / “pragmatic”
  Spoof higher layer contract.
  E.g.: per-IP-flow actions in Ethernet switches, MPLS LSR
What are better options to explore ?
Ethernet header
“contract” (CoS)
MPLS header
“contract” (EXP)
IP header
“contract” (TOS)
Higher Layers
/ Payload
Classical packet
Header stack
Ethernet header
MPLS header
IP header
“contract” (TOS)
Higher Layers
/ Payload
“Layer Violation”
spoof IP
spoof IP
Current Solutions

## Slide 13: “Contract” header options
Todays “correct” / “dogma”
  Every layer has it’s own contract header
  Mapping, duplication of standardization, loss of functionality,…
Todays “Layer violations” / “pragmatic”
  Spoof higher layer contract.
  E.g.: per-IP-flow actions in Ethernet switches, MPLS LSR
What are better options to explore ?
(1) New reuseable contract headers
  Support superset of service aspects of existing layers. Each layers instance may just be drop-in replacement of existing layer contracts for backward compatibility
  Benefit: allow definition of new contracts (e.g.: “DetNet” once – reuse same contract at L2, L3). Eliminate new work duplication
  Does not eliminate mapping betwen layers
Ethernet header
“contract” (CoS)
MPLS header
“contract” (EXP)
IP header
“contract” (TOS)
Higher Layers
/ Payload
Classical packet
Header stack
Ethernet header
MPLS header
IP header
“contract” (TOS)
Higher Layers
/ Payload
“Layer Violation”
spoof IP
spoof IP
Current Solutions
Higher Layers
/ Payload
Unified
Forwarding Plane
Contract headers
New contract Hdr
Ethernet header
New contract Hdr
MPLS header
New contract Hdr
IP header
Options to explore

## Slide 14: “Contract” header options
Todays “correct” / “dogma”
  Every layer has it’s own contract header
  Mapping, duplication of standardization, loss of functionality,…
Todays “Layer violations” / “pragmatic”
  Spoof higher layer contract.
  E.g.: per-IP-flow actions in Ethernet switches, MPLS LSR
What are better options to explore ?
(1) New reuseable contract headers
  Support superset of service aspects of existing layers. Each layers instance may just be drop-in replacement of existing layer contracts for backward compatibility
  Benefit: allow definition of new contracts (e.g.: “DetNet” once – reuse same contract at L2, L3). Eliminate new work duplication
  Does not eliminate mapping betwen layers
(2) Cross-layer semantic for contract header
  Single contract header can be sufficient
  Each node determines at which layer (e.g.: ethernet, MPLS, IP it operates), but uses same contract heder for hop-by-hops services
  Ideal when multiple layers used within single administrative entity (e.g.: IoT, Industry, Enterprise).
Ethernet header
“contract” (CoS)
MPLS header
“contract” (EXP)
IP header
“contract” (TOS)
Higher Layers
/ Payload
Classical packet
Header stack
Ethernet header
MPLS header
IP header
“contract” (TOS)
Higher Layers
/ Payload
“Layer Violation”
spoof IP
spoof IP
Current Solutions
Higher Layers
/ Payload
Unified
Forwarding Plane
Contract headers
New contract Hdr
Ethernet header
New contract Hdr
MPLS header
New contract Hdr
IP header
Higher Layers
/ Payload
New contract Hdr
Ethernet header
MPLS header
IP header
Cross-Layer Unified
Forwarding Plane
Contract header
Options to explore

## Slide 15: Full cross-layer re-useable packet headers / protocols
Learn from IPv6/SRv6 experience:
  SRv6 is attempt to reuse IPv6 at the layer previously occupied by MPLS/SR-MPLS
    “Network Layer”, compared to “Internet Layer” (IPv6 Internet end-to-end)
  Challenged by inheriting all aspects of Internet IPv6 into this layer… even when they do not match well:
    Large header overhead, long addresses, limited services (only packet steering, no better QoS). (“Hackery” to shorten address steering header ongoing in IETF...)
Creating a fully cross-layer reuseable protocol :
  More research / experimentation required
  Separating out the (QoS, High-Precision) Contract part and make that reuseable may be a good first goal!
  Replacing the “base header” (MPLS, Ethernet, IP) with common header requires variable length addresses, but also a lot more thought on migration, integration, optimization, ...

## Slide 16: Summary / Conclusions
Multiple per-hop forwarding layers are common today
  Sometimes beneficial, sometimes undesirable but today unavoidable
In a NewIP world these should be eliminated where not beneficial
A NewIP should be able to operate at multiple layers where beneficial
Per-hop services are ideally common across per-hop forwarding layers
Contract / Services packet headers ideally shareable across layers
Solving these challenges could be key for success of a New IP

## Slide 17: The End
Thank you for listening
Please reach out to us if you are interested in this topic
  Emails on title slide
Some References for further reading on next slide (sorry, incomplete).

## Slide 18: References
NewIP Packet headers:
  https://github.com/network2030/BPP (2020)
    Repository of papers about New IP contract header research papers.
    Also first research paper (NOMS 2020) about “Latency Based Forwarding”, a hop-by-hop service for Latency based SLO (Service Level Objectives), stateless latency management.
Differentiated / high precision traffic treatment (incomplete)
  https://github.com/network2030/lbf-poc (2020)
    Source code for LBF validation prototype
  https://tools.ietf.org/html/draft-stoica-diffserv-dps-02 (2003)
    Dynamic Packet State (DPS) – stateless, per-flow weighted fair bandwidth shaping.
  https://www.rfc-editor.org/rfc/rfc8698.txt
    NADA – Real time traffic congestion control with support of per-flow differentiated weights.
  Layered Internet Video Engineering (LIVE): Network-Assisted Bandwidth Sharing and Transient Loss Protection for Scalable Video Streaming, 2010 Proceedings IEEE INFOCOM
    Better than ECN congestion signaling
IPv6 routing solutions without need for (switched) L2 subnets
  RFC6550 (RPL), https://tools.ietf.org/html/draft-ietf-anima-autonomic-control-plane